## Slide 1: Network Topology
A network topology is the schematic arrangement of network elements, such as links and nodes.
The physical topology describes how devices on the network are connected.
The logical topology describes how data moves from one node to another.
Notes: Let’s start our discussion by understanding the definition of a network topology.
A network topology is the schematic arrangement of elements, such as links and nodes, which ultimately constitutes the structure of the network.
The physical topology describes how devices on the network are connected and the logical topology describes how data moves from one node to another.

## Slide 2
NVIDIA ACADEMY · VISUAL FOUNDATIONS
Topology Sample Library
Reference shapes, icons, and connection styles for InfiniBand topology diagrams.
Sample · 3 spines / 4 leaves
INSIDE
· Canonical 13-icon set
· Connection styles & colors
· Leaf-Spine · Fat-tree · Dragonfly+ · Torus 3D
· How to use this library
v0.1 · June 2026
academy-design@nvidia.com

## Slide 3
REFERENCE
Canonical Icon Set
Thirteen icons cover every InfiniBand topology diagram in the Academy curriculum.
NVIDIA Academy · Visual Foundations · Topology Sample Library
v0.1 · 2026
Switch
Switch + SM
Router
HCA
HCA
Network cloud
Storage
Fabric Admin
UFM
SM
UFM + SM
Server + SM
Server
GW
Gateway
Monitoring
Switch (3D)
SM
SM

## Slide 4
REFERENCE
Connection Styles & Colors
Line weight and color encode meaning. Use the same conventions across every diagram.
NVIDIA Academy · Visual Foundations · Topology Sample Library
v0.1 · 2026
Use
Sample
Spec
Default link
1.2pt · gray-500
Hot path / active
2.0pt · NVIDIA Green
Dimension X
1.5pt · NVIDIA Green
Dimension Y
1.5pt · Garnet
Dimension Z
1.5pt · CPU Blue
Fat-tree top tier
2.0pt · dark
Fat-tree bottom tier
1.0pt · dark
Inactive / fallback
1.0pt · dashed gray-500
SHAPE RULES
Square corners only.
1.2pt strokes by default.
White fill, dark gray stroke.
Use color to encode role,
not to decorate.

## Slide 5
SAMPLE
Topology · Leaf-Spine
Two tiers, fully meshed. Every leaf connects to every spine. Bisection bandwidth is uniform.
NVIDIA Academy · Visual Foundations · Topology Sample Library
v0.1 · 2026
Leaf-Spine · 3 spines × 4 leaves
Spine / Core
Leaf / Edge
SP-1
SP-2
SP-3
LF-1
LF-2
LF-3
LF-4
RULES
TIERS
Two. Spine + Leaf.
CONNECTIONS
Every leaf to every spine.
HOSTS
Connect only to leaves.
LINES
1.2pt gray. Hot path 2pt green.
LABELS
SP-n / LF-n. Role on the right.
USE WHEN
Predictable east-west traffic.

## Slide 6
SAMPLE
Topology · Fat-tree
Trunk gets fatter as you climb. Top-tier links are drawn 2pt; bottom-tier links 1pt.
NVIDIA Academy · Visual Foundations · Topology Sample Library
v0.1 · 2026
Fat-tree · 2 cores × 4 leaves × 8 hosts
Core
Leaf
Host
RULES
TIERS
Three. Core · Leaf · Host.
TOP TIER
Draw at 2pt — bandwidth is doubled.
BOTTOM TIER
Draw at 1pt — single link per host.
COLOR
Dark gray. Do not green-wash.
USE WHEN
All-to-all collectives at scale.

## Slide 7
SAMPLE
Topology · Dragonfly+
Groups of leaf-spine cells, fully meshed between groups in NVIDIA Green.
NVIDIA Academy · Visual Foundations · Topology Sample Library
v0.1 · 2026
Dragonfly+ · 3 groups (2 spines × 2 leaves each)
Group
Group
Group
RULES
INSIDE A GROUP
Leaf-spine bipartite. Gray 1.2pt.
BETWEEN GROUPS
Full mesh. NVIDIA Green 2.0pt.
VISUAL HIERARCHY
Green is the long-haul story.
USE WHEN
Very large clusters, low hop count.

## Slide 8
SAMPLE
Topology · Torus 3D
Isometric 2 × 2 × 2 grid. Each dimension uses its own color; dashed stubs at each corner mark the wraparound.
NVIDIA Academy · Visual Foundations · Topology Sample Library
v0.1 · 2026
Torus 3D · 2 × 2 × 2
+x
−x
+y
+z
AXES
+x NVIDIA Green
+y Garnet
+z CPU Blue
RULES
VIEW
Isometric. Do not rotate during narration.
EDGES
Color-encode the dimension.
WRAPAROUND
Dashed stubs in the axis color at each corner.
LABELS
+x / -x / +y / -y / +z / -z.
USE WHEN
Nearest-neighbor stencils, HPC physics.

## Slide 9
GUIDANCE
How to use this library
Copy shapes, then customize — the geometry is the contract, not the styling.
NVIDIA Academy · Visual Foundations · Topology Sample Library
v0.1 · 2026
01
Copy the geometry
Click into a sample, copy the shape group, paste into your deck. Keep relative positions and proportions intact.
02
Rename the labels
Replace SP-1/LF-1 with your real switch names. Keep label position, size, and Arial Bold 14pt.
03
Adjust counts, not styles
Add or remove rows of leaves/spines as needed. Do not change stroke weights, colors, or corner radii.
04
Encode meaning with color
Use NVIDIA Green for the hot path only. Reserve Garnet and CPU Blue for the second and third dimensions.
Full spec — naming, framing, labels, dimensions — at the Topologies page in the Visual Foundations portal.